## Slide 1: Video Compression
Presented By:
Mayank Roy
Sarvagya Mukhi
Riya Aggarwal
Shreya Gupta
Mentor :
Mr. Niteesh Sahni
Associate Mentors
Mr. Sarvesh Kumar
Ms. Dhanya

## Slide 2: VIDEO
A video is the technology of processing a sequence of still images representing scenes in motion.
Hence, any video can be divided into a number of images where each image represents a frame.

## Slide 3: THE NEED FOR COMPRESSION
Raw video contains an immense amount of data
Communication and storage capabilities are limited and expensive.
Example HDTV video signal  720x1280 pixels/frame progressive scanning at 60 frames/sec. (720 x 1280 pixel/frame) X (60 frames/sec) X (3 colors/pixel ) X ( 8bits/color ) = 1.3 Gb/sec !!!
20 Mb/s HDTV channel bandwidth !!
Requires compression by a factor of 70 .

## Slide 4: IMAGE
A digital image consists of pixels with color intensity values for red, green and blue(rgb format). These values together make up a 3-D matrix consisting of three planes.

## Slide 5: IMAGE
An LUVMAP image is an M-by-3 matrix that contains the NTSC luminance (L) and chrominance (U and V) colour components as columns that are equivalent to the colours in the RGB colour map.
Notes: National Television System Committee

## Slide 6: IMAGE
The image on the right shows the L plane of the original image (left).
The L plane consisting of the luminance values returns a grayscale version of the image.
A grayscale image is really just a 2-D matrix whose entries correspond to pixel intensity value.

## Slide 7
If an image has M rows and N columns of pixels, then we identify it as a matrix V of dimensions M x N.
This matrix V is a vector space.
A vector space is a non-empty set which follows the properties of addition “+” and multiplication “.”.
Image as a vector space
Notes: A vector space V is a non empty set with two operations addition “+” and multiplication “.” by scalars such that the following conditions are satisfied for any x,y,z ϵ V and α , β in F :
x + y = y + x
(x + y) + z = x + (y + z)
x+z = y has unique solution z for each pair (x,y).
α(βx) = (αβ)x
(α+β)x = αx+βx
α(x + y) = αx + αy
1.x = x

## Slide 8: IMAGE AS A VECTOR SPACE
Figures 1 & 2 represent addition operation acted upon the above image.
Figure 1  image + 80
Figure 2  image – 20
Thus the image can be treated as a vector space where the specified magnitude gets added/subtracted from the original intensity values.
Figure 1
Figure 2

## Slide 9: INNER PRODUCT SPACE
A vector space along with an inner product (dot/scalar product) is called an inner product space.
Inner product of u & v ϵ V (vector space) denoted by <u,v> which returns a scalar value.

## Slide 10: BASIS OF A VECTOR
Basis : Suppose S={v1,v2,….,vn} is a linearly independent set of vectors from the vector space V. Then S is called a basis (plural is bases) for V if any w ϵ V can be expressed as
w= a1v1 + a2v2 + ….. + anvn
where a1,a2,…,an are scalars.
Orthonormal basis:
An orthonormal basis for an inner product space is a basis whose elements are pairwise orthogonal
i.e. <xi,xj> = 0 when i≠ j.
and <xi,xj>= 1 when i=j.

## Slide 11: FOURIER BASIS & TRANSFORM
Two special ortho normal bases :
  Standard orthonormal basis
  Fourier basis
Standard orthonormal basis {e0,e1,…eN-1} where en [k]=0 when n ≠ k and en[n]=1 .
Fourier basis {f0,f1,…fN-1} for l2(ZN) is defined as follows :
fn [k]=exp ( 2Πikn/N ) / √N
If we express a vector v as a span of its Fourier basis viz.
v= a0f0+ a1f1+…….+anfn
Then the set of scalars [a0 a1 …… an]
forms the Fourier transform F(v) of v.

## Slide 12: SINGULAR VALUE DECOMPOSITION
Every matrix can be decomposed into 3 different matrices, say U D V where D is a diagonal matrix containing singular values and U & V are unitary matrices whose columns are singular vectors, as shown :
A=U*D*VT
Notes: Let A ϵ Rmxn . Then there exist orthogonal matrices U ϵ Rmxm and V ϵ Rnxn such that matrix A can be decomposed as follows :
A = U ∑ VT
where ∑ is and m x n diagonal matrix of form :
and a1 ≥ a2 ≥….. ≥ ap ≥ 0
The { ai } are termed as the singular values of matrix A.
The column of U are termed as left singular vectors while the column of V are termed as right singular vectors.

## Slide 13: SINGULAR VALUE DECOMPOSITION
Using SVD, The Fourier transform can be easily computed as follows . Let A be decomposed as :
A+ = V D UT
where the matrix D takes the form :
Where the diagonal values of D are the Fourier coefficients and the matrices U and V are the Fourier basis.
Hence, SVD provides a means to compute the Fourier transform of a singular matrix.

## Slide 14: SPOT THE DIFFERENCE
ORIGINAL IMAGE (540 coefficients)
IMAGE RECONSTRUCTION USING ONLY 100 FOURIER COEFFICIENTS

## Slide 15: IMAGE RECONSTRUCTION
By addition of one Fourier coefficient at a time we can create a fairly good approximation of the original image where similarity increases with the number of Fourier coefficients.
ORIGINAL IMAGE (540 coefficients)
IMAGE RECONSTRUCTION USING ONLY 15 FOURIER COEFFICIENTS

## Slide 16: IMAGE RECONSTRUCTION
40 Fourier coefficients
100 Fourier coefficients

## Slide 17: IMAGE RECONSTRUCTION
Therefore by using only 100 Fourier coefficients we can get a fairly good approximation of the original image having 540 Fourier coefficients.
On rebundling these compressed images we obtain a video requiring much less data.
150 Fourier coefficients

## Slide 18: Video compression
READING THE VIDEO
Breaking the video into Frames
Storing Every Frame in an array of Structures
Processing Each Frame and then applying the compression algorithm
Rebundling the compressed images into a new array of structures
Converting back to a movie
VIDEO RECONSTRUCTED WITH MUCH LESS DATA THAN ORIGINAL VIDEO

## Slide 19
THANK YOU